## Slide 1
Enhanced Base-Delta Compression with Memory Pooling
Aditya Bhandaru, Gennady Pekhimenko, Onur Mutlu
Overview
Motivation
Mechanisms
Results
Conclusions
Base-Delta Compression [Pekhimenko et. al., PACT’12] proposes a promising technique for increasing on chip cache capacity using compression.
B+Δ offers good compression but incurs an additional access latency.
B+Δ suffers poor compressibility when adjacent data in memory have large value ranges.
Observation: Traditional compilers and memory-allocators are unaware of B+Δ cache compression in hardware.
Key Idea: Arrange data in memory to optimize B+Δ compressibility.
Solution: Recent literature on Memory Pooling, Data Splitting [Curial et. al., ISMM’08] and related work seems promising.
Problem: Can we mitigate low compressibility cases for B+Δ compression?
Increase viability for B+Δ implementation in hardware, and justify the extra access latency.
Proposals like Memory Pooling and Data Splitting already improve locality and reduce value range in adjacent data values.
But they have not yet been applied to B+Δ!
BΔ-POOL: Strong improvement over baseline, pooling and base-delta
Just proof of concept*
Makes single base version of BΔI more viable.
*Recall that splitting and pooling was done by hand. Safely splitting-pooling in the compiler is not always possible.
Further Work
Implement pointer transformations in LLVM.
Run benchmarks on cycle accurate BΔ-simulator.
Incorporate data from standard benchmarks.
Multithreaded environments.
Interaction with non-traditional LRU policies.
See CARP by Huberty et. al.
Chart: Effect of Pooling on B+Δ Compression Block Types
| bisort | bisort.pool | llu | llu.pool | sort | sort.pool
LARGE | 767 | 488 | 1763 | 28 | 251 | 80
MEDIUM | 253 | 152 | 345 | 624 | 0 | 0
REPEATED | 0 | 0 | 0 | 97 | 0 | 0
ZEROS | 4 | 0 | 0 | 833 | 0 | 125
Figure 1. Each column shows the ratio of block-types for B+D compression with and without splitting and pooling. Notice the large increase in 1-byte all-zero blocks, and general decrease of large, uncompressed blocks. (1 MB, 16-way, 32-BiB BΔ-Cache)
Basic Splitting-Pooling Example (64-bit)
FLAG (1B)
VAL (4B)
POINTER (8B)
Simple struct (a node perhaps)
In memory layout (high range in adjacent values)
After split-pool allocation (much lower range)
Proof of Concept Methodology
To test the affect of splitting and pooling on B+Δ compression, we manually restructured programs for optimal data layout. (Later: implement pointer transformations in compiler)
For this project, we focused on pointer based algorithms for benchmarks (bisort and llu – an apprx. for Health)
After B+Δ compression (huge space savings)
B0
+0
+1
…
B0x77..0
+0
…
+0x0
+0x4
+0xC
…
B100
+0
+8
-7
…
0
100
0x77..0
1
108
0x77..4
0
93
0x77..C
…
…
0
1
0
0x77..0
0x77..4
0x77..C
100
108
93
…
…
…
…
Results for LLU micro-benchmark (working set ~117kb)
Chart: 
| 16KB | 32KB | 64KB | 128KB | 256KB | 512KB
BASELINE | 1 | 1 | 1 | 1
POOLING | 0.90873 | 0.94839 | 1.0189 | 1.0003
BASE-DELTA | 1.0744 | 0.98434 | 1.0134 | 1
BD+POOL | 1.1487 | 1.0642 | 1.0311 | 1.0003
Chart: 
| 16KB | 32KB | 64KB | 128KB | 256KB | 512KB
BASELINE | 1 | 1 | 1 | 1
POOLING | 1 | 1 | 1 | 1.481
BASE-DELTA | 1 | 1 | 1 | 1.0089
BD+POOL | 1.3773 | 1.4297 | 2.433 | 4.4479
Normalize Hit Ratio by Cache Size
Normalized Compression Ratio by Cache Size
Improvement in hit% from fewer evictions (more space)
B+Δ alone reaches cache capacity for sizes < working set.
BΔ+POOL still comes up with space savings!
Compression Ratio: 2.6x avg (over LLU, TreeSort, ArraySort) 1.93x over just Split-Pool, 2.47x over only B+Δ
Hit Rate: 8% avg. increase over micro-benchmarks.
Pointer based algorithms had poor locality.
Expect multithreaded apps benefit from compression too.