## Slide 1
Enhanced Base-Delta Compression with Memory Pooling
Aditya Bhandaru, Gennady Pekhimenko, Onur Mutlu
Overview
Motivation
Mechanisms
Results
Conclusions
Base-Delta Compression [Pekhimenko et. al., PACT’12] proposes a promising technique for increasing on chip cache capacity using compression.
B+Δ offers good compression but incurs an additional access latency.
B+Δ suffers poor compressibility when adjacent data in memory have large value ranges.
Observation: Traditional compilers and memory-allocators are unaware of B+Δ cache compression in hardware.
Key Idea: Arrange data in memory to optimize B+Δ compressibility.
Solution: Recent literature on Memory Pooling and Data Splitting [Curial et. al., ISMM’08] and related work seem promising.
Problem: Can we mitigate low compressibility cases for B+Δ compression?
Increase viability for B+Δ implementation in hardware, and justify the extra access latency.
Proposals like Memory Pooling and Data Splitting already improve locality and reduce value range in adjacent data values.
But they have not yet been applied to B+Δ!
Min-Eviction: a novel replacement policy for the compressed cache
Outperforms current state-of-the-art replacement policies
First to consider both compressed block size and probability of reuse
Simple to implement
Further Work:
Global Min-Eviction: a global replacement policy for the compressed decoupled variable way cache that applies similar insight as Min-Eviction
Fairness in compressed cache replacement
Multi-core evaluation and analysis (see paper): 4% increase in normalized weighted speedup over LRU in heterogeneous workloads
Chart: Effect of Pooling on B+Δ Compression Block Types
| bisort | bisort.pool | llu | llu.pool | sort | sort.pool
LARGE | 767 | 488 | 1763 | 28 | 251 | 80
MEDIUM | 253 | 152 | 345 | 624 | 0 | 0
REPEATED | 0 | 0 | 0 | 97 | 0 | 0
ZEROS | 4 | 0 | 0 | 833 | 0 | 125
Figure 1. Each column shows the ratio of block-types for B+D compression with and without splitting and pooling. Notice the large increase in 1-byte all-zero blocks, and general decrease of large, uncompressed blocks.
Basic Splitting-Pooling Example (64-bit)
FLAG (1B)
VAL (4B)
POINTER (8B)
Simple struct (a node perhaps)
In memory layout (high range in adjacent values)
0
100
0x77..0
1
108
0x77..4
0
93
0x77..C
…
…
0
1
0
…
0x77..0
0x77..4
0x77..C
…
…
100
108
93
…
After split-pool allocation (much lower range)
Proof of Concept Methodology
To test the affect of splitting and pooling on B+Δ compression, we manually restructured programs for optimal data layout.
Ideally these pointer transformations will be implemented in the compiler.
Chart: Normalized Compression Ratio for Benchmarks
| bisort | llu | sort
BASELINE | 1 | 1 | 1
POOLING | 1.6 | 1.3273 | 1.2244
BASE-DELTA | 1.1448 | 1.102 | 1.0502
BD+POOL | 1.8156 | 3.7274 | 2.2613
B+Δ compression on a 2MB, 16-way, 32BiB cache.